## Slide 1: CSE5095-002: Topics in Software Defined Networking
Lecture 11
SDN security
Minmei Wang
Computer Science and Engineering

## Slide 2: SDN architecture

## Slide 3: Attacks to the SDN architecture
Flow Wars: Systemizing the Attack Surface and Defenses in Software-Defined Networks
Changhoon Yoon, Seungsoo Lee, Heedo Kang, Taejune Park, Seungwon Shin, Vinod Yegneswaran, Phillip Porras, Guofei Gu

## Slide 4: Overview of the SDN attack surface
CP-R: control plane remote attacks
CP-L: control plane local attacks
CC: control channel attacks
DP: data plane attacks

## Slide 5: CP-R: Control Plane Remote Attacks
Denial-of-Service (DoS) attacks
  SDN controllers
    Loss of availability or the instability of the victim network
Network-view manipulation
  Controllers implement Host Tracking Services (HTS) and Link Discovery Services (LDS)
    Since there are dynamically changing locations of the network nodes and hosts

## Slide 6: Denial-of-Service (DoS) attacks
Feasible remote DoS attacks
  Packet-in flooding (OpenFlow)
    An SDN switch notifies an SDN controller of each unseen flow (or for each flow table mismatch)
  Switch table flooding
    Fill up the switch table of controller and cause switch disconnections
      Floodlight: add one switch table entry when receiving OpenFlow’s features_reply meassage with new DPID values
    Use up all the memory resource available in the controller

## Slide 7: Denial-of-Service (DoS) attacks
Feasible remote DoS attacks
  Switch identification spoofing
    Modify the OpenFlow control message to spoof its identity as if it is the target switch
      DPID and the name of a switch are used to distinguish between switch devices
      Attackers use DPID and the name of a switch to build a connection, disconnecting the connection with the compromised switch (legitimate switch)
  Malformed control message injection
    Attackers modifies the message length field of the OpenFlow header to an incorrect value
    SDN controllers (e.g., POX and Floodlight) disconnect the switches that sent such malformed messages

## Slide 8: Denial-of-Service (DoS) attacks
Feasible remote DoS attacks
  System time manipulation
    SDN controllers and applications refer to system variables for various purposes (e.g., FloodLight and OpenDaylight)
      System time variables for carrying out time-sensitive tasks
        Calculate packet timeouts
      Modify time variables may cause disconnection between switches and controllers

## Slide 9: Denial-of-Service (DoS) attacks
System time modification causing switch disconnection
This attack does not affect POX because this controller does not refer to the system time

## Slide 10: Network-view manipulation
Topology poisoning attack
  Deceive the HTS of controllers
    Forge some network packets
      Most HTS implementations only use simple identifiers to distinguish among the hosts
Attacker A spoof packets to have the source MAC and IP of Web Server B
A sends packet_in based on manipulated traffic information
HTS believes that Web Server B has migrated and newly linked to port 1

## Slide 11: Overview of the SDN attack surface
CP-R: control plane remote attacks
CP-L: control plane local attacks
CC: control channel attacks
DP: data plane attacks

## Slide 12: CP-L: Control Plane Local Attacks
Arbitrary system termination
  A system call misuse scenario is possible since most SDN controllers are designed to run SDN applications within the controller instance
    An SDN application invokes the system exit command
      Terminate the application & controller instance
    Loss of the control plane is undesirable
System resource exhaustion
  SDN controller implementations are end-host user-level applications
  The performance is limited by the capabilities of the hosting machine
  It is possible to consume the system resources of the hosting machine
    A simple SDN application

## Slide 13: CP-L: Control Plane Local Attacks
Network service neutralization
  Control message delivery obstruction
    Packet-in unsubscription: different applications subscribe newly generated control events

## Slide 14: CP-L: Control Plane Local Attacks
Network service neutralization
  Control message delivery obstruction
    API misuse
  Service chain jamming
    Intentional insertion of infinite loops into the application
Service chain

## Slide 15: CP-L: Control Plane Local Attacks
Unauthorized application management
  An SDN application can misuse Northbound APIs to evict other legitimate applications
A malicious SDN application may legitimately call the function to terminate other application via Northbound API.
OpenDaylight

## Slide 16: CP-L: Control Plane Local Attacks
Unauthorized network control
  packet_in control message notifies an SDN controller of a newly incoming network flow
  It’s possible to manipulate the control plane by abusing those messages
Examples
  Flow-Rule modification

## Slide 17: CP-L: Control Plane Local Attacks

## Slide 18: CP-L: Control Plane Local Attacks
Examples
  Flow table flushing
It causes flow entry mismatch for all incoming network flows and degrade the network performance

## Slide 19: CP-L: Control Plane Local Attacks
Unauthorized network-view manipulation
  SDN controllers implement a shared internal database for storage and management of network information
  No restricted access or modifications to the internal storage
Internal data storage modification

## Slide 20: Overview of the SDN attack surface
CP-R: control plane remote attacks
CP-L: control plane local attacks
CC: control channel attacks
DP: data plane attacks

## Slide 21: CC: Control Channel Attacks
Eavesdropping
  Encrypted channel (e.g., SSL/TLS protocol) is not widely adopted
  Attackers can sniff the ongoing OpenFlow messages
    Exfiltrate the topology information of the managed network
Man-in-the-Middle

## Slide 22: Overview of the SDN attack surface
CP-R: control plane remote attacks
CP-L: control plane local attacks
CC: control channel attacks
DP: data plane attacks

## Slide 23: DP: Data Plane Attacks
Flow rule flooding
  No restriction on issuing control messages
    An SDN application can issue any control message at any time
  A malicious application continuously generates flow rules
    Fill up the flow table of the switch
    The switch cannot handle more rules
Switch firmware abuse
  A malicious application install flow rules that need to be processed in a software table
    Network performance degradation

## Slide 24: DP: Data Plane Attacks
Switch firmware abuse

## Slide 25: DP: Data Plane Attacks
Malformed control message injection
  Manipulated control messages may be sent to the data plane
    Cause switch to end up in an unpredictable state
      SDN controllers (e.g., POX and Floodlight) disconnect the switches that sent such malformed messages
Data leakage
  OpenFlow-enabled switches query SDN controllers for each flow table miss
    Infer sensitive information by measuring RTT
      J. Sonchack, A. Dubey, A. J. Aviv, J. M. Smith, and E. Keller, “Timing based
reconnaissance and defense in software-defined networks.