## Slide 1: TEA: Enabling State-Intensive Network Functions on Programmable Switches
Daehyeok Kim§‡
Zaoxing Liu§, Yibo Zhu^, Changhoon Kim†, Jeongkeun Lee†, Vyas Sekar§, Srinivasan Seshan§
§Carnegie Mellon University
†Intel, Barefoot Switch Division
‡Microsoft Research
^ByteDance Inc

## Slide 2: Network functions in the network
Network functions (NFs) are an essential component
E.g., Load balancer, Firewall, Network address translator (NAT), …
NF performance and scalability are key challenges

## Slide 3: Approaches to deploying network functions
Commodity server
Virtualization layer
NAT
LB
FW
NAT | LB | FW
Programmable switch ASIC |  | 
NAT
LB
FW
Standalone hardware Fixed-function Performance: O(10 Gbps) Memory: O(10GB) DRAM
Price: >$40K
Server-based Software (NFV)
Programmable Performance: O(10 Gbps) Memory: O(10GB) DRAM
Price: $3K
Switch-based NF Programmable Performance: O(1 Tbps) Memory: O(10MB) SRAM
Price: $10K
Notes: Terabyte per second level
Implementing them on a cluster of commodity servers

## Slide 4: Problem: serving demanding workloads
None of the options can efficiently serve demanding workloads!
Millions of concurrent flows (O(100MB)) + high traffic rate (> 1 Tbps)
NAT LB FW
Programmable switch ASIC
NAT
NAT LB FW
FW LB Virtualization layer Commodity server
Promising but cannot maintain flow state 
Standalone hardware Fixed-function Performance: O(10 Gbps) Memory: O(10GB) DRAM
Price: >$40K
Server-based Software (NFV)
Programmable Performance: O(10 Gbps) Memory: O(10GB) DRAM
Price: $3K
Cost- and energy-inefficient 
Switch-based NF Programmable Performance: O(1 Tbps) Memory: O(10MB) SRAM
Price: $10K

## Slide 5: Root cause: limited on-chip SRAM
Limited on-chip SRAM space: O(10MB)
Infeasible to maintain large flow state within on-chip SRAM
E.g., LB state for 10M flows requires ≈100MB
Adding more SRAM would be too expensive 
Can we leverage larger and cheaper DRAM near switch ASICs?

## Slide 6: DRAM available on a switch board
Switch data plane (ASIC)
Pipeline stages On-chip SRAM
Switch board
Switch control plane
DRAM
Limited scalability in terms of size and access bandwidth
High cost
CPU
Option #1:
DRAM on the switch control plane
Option #2:
On-board, off-chip DRAM
PCIe
Switch board
Switch control plane
Switch data plane (ASIC)
Pipeline stages On-chip SRAM
DRAM
Extension
Notes: ASIC on the data plane can access DRAM on the control plane by PCIe channel. But the PCIe channel has a limited bandwidth, which is
lower than the ASIC’s per-port bandwidth.
The paper states that the on-board off-chip DRAM has limitation on the size and memory access bandwidth

## Slide 7: Opportunity: DRAM on commodity servers
+ Scalable memory size and bandwidth
+ Low cost
Switch board
Switch control plane
Switch data plane (ASIC)
Pipeline stages On-chip SRAM
Server
DRAM

## Slide 8: Table Extension Architecture (TEA)
Switch data plane (ASIC)
Switch board
Switch control plane
Pipeline stages
On-chip SRAM
Server
DRAM
Virtual table abstraction for state-intensive NFs using external DRAM on servers
Table lookups with low and predictable latency
and scalable throughput
APIs that allow easy integration with NFs
Key Value

## Slide 9: Outline
Motivation
TEA design
Results

## Slide 10: TEA design overview
NF Impl.
+ TEA P4 API
P4 Compiler
Developer
Switch data plane (ASIC)
Switch board
Switch control plane
Pipeline stages
On-chip SRAM
Server
DRAM
Binary

## Slide 11: Challenge 1: Enabling external DRAM access from switch ASIC
Strawman: accessing external DRAM via the control plane
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Packet
11
Limited access bandwidth
High and unpredictable latency 

## Slide 12: Challenge 1: Enabling external DRAM access from switch ASIC
Switch data plane (ASIC)
Switch board
Switch control plane
Server
DRAM
On-chip SRAM
How to enable switch ASIC to directly access external DRAM without CPUs and hardware modifications?
Packet
11

## Slide 13: Challenge 2: Enabling single round-trip table lookup
Key Value
5-tuple
Addr.
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
How to ensure a correct table entry can be retrieved
in a single memory access?

## Slide 14: Challenge 3: Deferred packet processing
Key Value
5-tuple
Addr.
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
How to defer packet processing during lookups
without stalling the pipeline or buffering at the switch?

## Slide 15: Challenge 4: Scaling TEA with multiple servers
With a single server, scalability and availability can be limited
Server
DRAM
A single server can fail
Switch data plane (ASIC)
Switch board
Switch control plane
Packet
On-chip SRAM
Access bandwidth is limited to a single link
14

## Slide 16: Challenge 4: Scaling TEA with multiple servers
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
Packet
How to deal with servers’ availability changes?
On-chip SRAM
How to balance access loads across servers?
14

## Slide 17: Challenge 1: How to access external DRAM in the data plane?
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Packet
Switch ASICs do not have direct external DRAM access capability!
Is it possible to enable ASICs to access external DRAM
without hardware modifications and CPU involvement?

## Slide 18: Direct Memory Access(DMA)
DMA allows certain hardware subsystems to access main system memory independently
of the CPU
PIO (Programmed Input/Output) Data transfer
Processor
System Bus
Memory
Peripheral 1
Peripheral 2
Memory -> peripheral 1

## Slide 19: Direct Memory Access(DMA)
DMA allows certain hardware subsystems to access main system memory independently
of the CPU
DMA Data transfer
Processor
System Bus
Memory
Peripheral 1
Peripheral 2
DMA controller

## Slide 20: Direct Memory Access(DMA)
DMA allows certain hardware subsystems to access main system memory independently
of the CPU
DMA Data transfer
Processor
System Bus
Memory
Peripheral 1
Peripheral 2
DMA controller
Arbitrator
Grant
Req
Req
Grant
Peripheral 1 request the service of DMA
DMA controller requests for the buses
DMA gets the buses and activates DMAK
DMA starts to transfer data from memory to peripheral 1
DMA tells the CPU it finishes

## Slide 21: Remote Direct Memory Access(RDMA)
RDMA is a direct memory access from the memory of one computer into that of another
without involving either one's operating system.

## Slide 22: Enabling RDMA in the switch data plane
Key idea: Crafting RDMA packets using ASIC’s programmability
1. A packet comes into the pipeline
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Packet
16

## Slide 23: Enabling RDMA in the switch data plane
Key idea: Crafting RDMA packets using ASIC’s programmability
1. A packet comes into the pipeline
2. The ASIC adds RDMA headers to craft an RDMA request
Switch board
Switch control plane
Server
DRAM
Switch data plane (ASIC)
RDMA-H Packet
On-chip SRAM
16

## Slide 24
Key idea: Crafting RDMA packets using ASIC’s programmability
1. A packet comes into the pipeline
2. The ASIC adds RDMA headers to craft an RDMA request
3. The server NIC replies as it would for any standard RDMA request
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Payload
RDMA-H
16
Enabling RDMA in the switch data plane

## Slide 25
Key idea: Crafting RDMA packets using ASIC’s programmability
1. A packet comes into the pipeline
2. The ASIC adds RDMA headers to craft an RDMA request
3. The server NIC replies as it would for any standard RDMA request
4. The ASIC parses the response
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Payload
16
Enabling RDMA in the switch data plane

## Slide 26: Enabling RDMA in the switch data plane
Key idea: Crafting RDMA packets using ASIC’s programmability
1. A packet comes into the pipeline
2. The ASIC adds RDMA headers to craft an RDMA request
3. The server NIC replies as it would for any standard RDMA
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Server
DRAM
Payload
Simple switch-side flow control prevents buffer overflows at the NIC!
-> simplified transport is enough
4. The ASIC parses the response
16

## Slide 27: Enabling RDMA in the switch data plane
The needed metadata is provided via the control plane in advance
RoCE: RDMA over converged Ethernet

## Slide 28: Challenge 2: Single round-trip table lookups
Switch data plane (ASIC)
Switch board
Switch control plane
Server
DRAM
Packet
On-chip SRAM
RDMA read takes ~2μs: multiple accesses can result in
high and unpredictable table lookup latency 
Can we enable external table lookups in a single round trip?
i.e., we need O(1) lookup mechanism

## Slide 29: Cuckoo hashing as a potential approach
Cuckoo hash table in DRAM
Server
DRAM
Switch board
Switch control plane
Switch data plane (ASIC)
On-chip SRAM
Packet
18

## Slide 30
Cuckoo Hash Table
buckets
slots
()

## Slide 31: Cuckoo hashing as a potential approach
Cuckoo hash table in DRAM
Can we enable table lookup with a single memory access?
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
hash
1
(x)
hash
18
2
(x)

## Slide 32: TEA-table: lookup data structure
TEA-table in DRAM
Server
DRAM
Key idea: Repurposing bounded linear probing (BLP)
Designed for improving cache hit rate in software switch [Zhuo’19*]
Switch board
Switch control plane
Switch data plane (ASIC)
On-chip SRAM
Packet
*Dong Zhou. Data Structure Engineering for High Performance Software Packet Processing. Ph.D. Dissertation. Carnegie Mellon University, 2019.
19

## Slide 33: TEA-table: lookup data structure
TEA-table in DRAM
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
Key idea: Repurposing bounded linear probing (BLP)
Trading space efficiency
for contiguous allocation
19
Colliding entries are stored in the switch SRAM

## Slide 34: TEA-table: lookup data structure
TEA-table in DRAM
Server
DRAM
Key idea: Repurposing bounded linear probing (BLP)
Can read two buckets in one RDMA read!
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
hash (x)
19

## Slide 35: Challenge 3: Deferred packet processing
Switch data plane (ASIC)
Switch board
Switch control plane
Server
DRAM
Packet
On-chip SRAM
Packet processing needs to be
deferred until a lookup completes
Can we defer only a select packet without stalling the pipeline?

## Slide 36: Offloading packet store to TEA-table for asynchronous packet processing
Idea #1: Employing scratchpad in TEA-table to buffer packets
Scratchpad
TEA-table in DRAM
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
21

## Slide 37: Offloading packet store to TEA-table for asynchronous packet processing
Idea #1: Employing scratchpad in TEA-table to buffer packets
 |  | Packet
Scratchpad
TEA-table in DRAM
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
RDMA-Write Packet
21

## Slide 38: Offloading packet store to TEA-table for asynchronous packet processing
Idea #1: Employing scratchpad in TEA-table to buffer packets
Scratchpad
Packet
TEA-table in DRAM
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
RDMA-Read
21

## Slide 39: Offloading packet store to TEA-table for asynchronous packet processing
Idea #1: Employing scratchpad in TEA-table to buffer packets
Scratchpad
Packet
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
Packet
On-chip
Due to the ASIC’s parser limitation, the original packet and the bucket cannot be parsed
TEA-table in DRAM
Notes: High- speed switching ASICs usually can parse only the first few hundreds of bytes in each packet.

## Slide 40: Offloading packet store to TEA-table for asynchronous packet processing
Idea #2: Employing shadow table in TEA-table
Scratchpad
 |  |  |  | Packet
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Shadow table
Slightly increase of DRAM usage
22

## Slide 41: Offloading packet store to TEA-table for asynchronous packet processing
Idea #2: Employing shadow table in TEA-table
Scratchpad
Packet
Server
DRAM
Shadow table
Switch data plane (ASIC)
Switch board
Switch control plane
Packet
On-chip SRAM
The ASIC can parse the buckets and process the packet
22
with a right table entry 

## Slide 42: Challenge 4: Scaling TEA with multiple servers
Server
DRAM
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet
Small on-chip cache for load balancing and higher throughput: cache at least popular packets (N is the number of servers)
Repurpose ASICs’ capability for reacting servers’ availability changes
Split hash tables into N sub-tables and distribute them into N servers
Check utilization and port status by repurposing the meter and packet generator engine of the switch ASIC
Notes: Control plane to check link utilization and port status; utilize meter and packet generator engine of ASIC to check the state of servers

## Slide 43: Putting it all together
Leveraging programmability of ASICs
for accessing external DRAM in the data plane
TEA provides a virtual table abstraction to state-intensive NFs
Repurposing BLP for constant time lookup
Small on-chip cache
for scalability
Server
DRAM
Offloading packet store for async. packet processing
Switch data plane (ASIC)
Switch board
Switch control plane
On-chip SRAM
Packet

## Slide 44: Putting it all together

## Slide 45: Outline
Motivation
TEA design
Results

## Slide 46: Implementation and evaluation setup
Implemented TEA API as P4 modules (aka. control block in P4)
Implemented canonical NFs including NAT and stateful firewall
- Load 10 million table entries
Testbed setup: Tofino-based switch + 12 servers with RDMA NICs

## Slide 47: Does TEA access channel provide low and predictable lookup latency?
2
1
0
3
64
128
256 512
Packet size (bytes)
1024
1500
Latency (us)
TEA RDMA-read
Each lookup takes 1.8-2.2 us and the latency grows with the packet size

## Slide 48: Does TEA access channel provide low and predictable lookup latency?
The server NIC can handle 7.3-10.9 million lookups per second

## Slide 49: Does TEA provide scalable throughput?
0
50
100
150
1
2 4
Number of DRAM servers
8
Million lookups / second
No cache
Uniform
α=0.95
α=0.99 Traffic generation rate
Notes: The skewness of the flow and cache influences the reuslt

## Slide 50: Other results
Cost efficiency of TEA-enabled NFs compared to server- based counterparts.
Handling server failures within a second with a slight throughput degradation
Less than 9% of switch ASIC resource usage
See paper for more details!

## Slide 51: Conclusion
Limited on-chip memory restricts potentials of switch-based NFs
Table Extension Architecture for Programmable Switches:
RDMA-based external DRAM access
BLP-based efficient lookup table structure
Asynchronous packet processing by offloading packet store
Small on-chip cache for scalability
Provides low and predictable latency with scalable throughput
Latency: 1.8 - 2.2 μs
Throughput: 138 million lookups/sec with 8 servers

## Slide 52: How does TEA affect NF processing latency?
0
0.5
0
1 2
Processing latency (μs)
3
CDF
Served by on-chip cache
Served by TEA-table
Flow size skewness (α) affects on-chip cache hit rate
Baseline (SRAM only) Uniform α=0.9 α=0.99 Real 1
Notes: Navy blue