## Slide 1: NetVRM: Virtual Register Memory for Programmable Networks
Hang Zhu
Tao Wang, Yi Hong, Dan R. K. Ports, Anirudh Sivaraman, Xin Jin

## Slide 2: Data plane objects
Registers enable a new class of
reg-stateful applications
Stateless (lifespan <= 1 packet)
Metadata, packet headers
Stateful (lifespan > 1 packet)
Tables, counters, meters, registers
2

## Slide 3: Registers in P4
Registers are stateful memories whose values can be read and written in actions.
3
c11 |  | 
d estimators per array
m arrays
c12 |  | 
c13 |  | 
c14 |  | 
Counter:
Count-Min Sketch
Counter: return minimum
Implemented by registers in P4

## Slide 4: Registers in P4
Register memory is implemented with standard SRRM blocks.
Register can be read by both the control plane and data plane.

## Slide 5: The case of dynamic allocation for register memory
5
Necessity
  Limited register memory (e.g., a few Mb/stage)
  Concurrent reg-stateful applications
Potential benefits
  Most applications can operate with different amounts of available memory
  Diminishing return

## Slide 6: Diminishing return
6
NetCache caches hot objects in the switch data plane
Store flow records in the data plane.
Hash collisions caused by inadequate memory require additional control plane processing.

## Slide 7: Diminishing return
Diminishing return: the benefit of additional memory decreases with the amount of allocated memory
NetCache with different skewed workload
0.28->0.36: 768 register slots
0.36->0.46: 3072 register slots
7

## Slide 8: Existing solutions and limitations
Static binding of register memory
Ignore hardware constraints
No network-wide dynamic allocation
8
Merged in compilation time
P4Visor [CoNEXT’18]
BMv2
Hyper4 [CoNEXT’16]
Allocation in a single switch
Support multiple applications on a programmable switch

## Slide 9: Realizing dynamic register memory allocation
How to enable online allocation
How to modify P4 programs
How to maximize multiplexing benefits
Virtual register memory
P4VRM compiler Dynamic allocation
9

## Slide 10: NetVRM architecture
xx.p4vrm
Run-time API
App 1
Virtual Register Memory
App 3
…
zoom in
Dynamic Memory Allocation
NetVRM
App 2
Network
Data Plane
Control Plane
P4VRM
Compiler
xx.p4vrm
A network management system that supports dynamic register memory sharing between multiple concurrent applications on a programmable network
Expose a virtual register memory abstraction to applications
Dynamically allocate memory for multiple applications and try to satisfy as many application’s requirements as possible
Develop and compile P4 programs with virtual register memory.

## Slide 11: Virtual register memory
Page tables
Counter record
App 1
App 2
App 3
Virtual Register Memory
Page Table
App
Virtual Array
NetVRM
Data Plane
Match | Action
app=1 | offset=0, size=16k
app=2 | offset=16k, size=16k
app=3 | offset=32k, size=32k
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
Control Plane
Page Table
Multi-stage Physical Register Arrays
Counter Record
total_cnt
hit_cnt
total_cnt
hit_cnt
total_cnt
hit_cnt
…
…
Counter Record
Parameters are configured by the control plane at runtime

## Slide 12: Address translation
0 | 2 | 4 |  | 6
1 | 3 | 5 |  | 7
size = 2, offset= 1 VA= 5 → PA= (2, 2)
Translation formula
0 1 2 3
0
1
2
3
4
5
6
7
physical array index
physical slot index
VA=6 -> PA=(3,1)

## Slide 13: Virtual register memory
Page tables
Counter record
App 1
App 2
App 3
Virtual Register Memory
Page Table
App
Virtual Array
NetVRM
Data Plane
Match | Action
app=1 | offset=0, size=16k
app=2 | offset=16k, size=16k
app=3 | offset=32k, size=32k
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
0
…
16k
…
32k
…
…
…
Control Plane
Page Table
Multi-stage Physical Register Arrays
Counter Record
total_cnt
hit_cnt
total_cnt
hit_cnt
total_cnt
hit_cnt
…
…
Counter Record
Parameters are configured by the control plane at runtime
The total number of packets for the application
The number of packets that hits the switch register memory
Real time hit ratios

## Slide 14: NetVRM architecture
xx.p4vrm
Run-time API
App 1
Virtual Register Memory
App 3
…
zoom in
Dynamic Memory Allocation
NetVRM
App 2
Network
Data Plane
Control Plane
P4VRM
Compiler
xx.p4vrm
Dynamically allocate memory for multiple applications and try to satisfy as many application’s requirements as possible

## Slide 15: Scope of dynamic resource allocation
Work with a variable amount of register memory
Overcome insufficient register memory with a fallback mechanism
Elastic applications Inelastic applications
Require a fixed amount of register memory
Cannot work with less
support
benefit

## Slide 16: Dynamic resource allocation
Polls the counter from the data plane
Obtains the utility
Dynamically allocates the register memory for each application based on utility
Elastic applications Inelastic applications
benefit

## Slide 17: Problem formulation
Objective
Maximize number of applications with satisfied utility target
Constraints
Register memory constraints on each switch
Virtual register memory size of c switches as

## Slide 18: Challenges for dynamic resource allocation
Definition of application utility
Unknown and dynamic utility functions
Multiple paths of an application
Memory hit ratio by default

## Slide 19: Memory hit ratio by default
Application-agnostic
Reflect application-level performance
Computed online
n packets
m packets processed
by register memory
Fallback mechanism
n-m packets
Hit ratio =

## Slide 20: Challenges for dynamic resource allocation
Unknown and dynamic utility functions
Online utility curve estimation

## Slide 21: Online utility curve estimation
cf>1: compensate for the diminishing return
The amount of memory that can be moved
The amount of memory to be added

## Slide 22: Dynamic resource allocation
Multiple paths of an application
Network-wide register memory allocation
Step 1: decompose over_mem and under_mem
Step 2: over_mem -> under_mem
At the end of each allocation epoch, NetVRM fetches counters, computes the online utilities, and then make the new memory allocation plan.

## Slide 23: NetVRM architecture
xx.p4vrm
Run-time API
App 1
Virtual Register Memory
App 3
…
zoom in
Dynamic Memory Allocation
NetVRM
App 2
Network
Data Plane
Control Plane
P4VRM
Compiler
xx.p4vrm
Develop and compile P4 programs with virtual register memory.

## Slide 24: P4VRM compiler
.p4 with VRM
p4vrm compiler
.cpp for
updates
…
heavy_hitter
.p4vrm
netcache
.p4vrm
…
heavy_hitter
.p4
netcache
.p4
Step 1: developers extend .p4 to .p4vrm
developers
Mark the register arrays and related
declarations as virtualized

## Slide 25: P4VRM compiler
p4vrm compiler
.p4 with VRM
.cpp for updates
…
heavy_hitter
.p4vrm
netcache
.p4vrm
…
heavy_hitter
.p4
netcache
.p4
Step 2: compiler outputs .p4 and .cpp
Step 1: developers extend .p4 to .p4vrm
developers
Control plane APIs for resetting counters, fetching counters, resetting memory and configuring the virtual memory

## Slide 26: Implementation
6.5 Tbps Intel Tofino switch
Four emulated switches with four independent pipelines
P4VRM compiler
  built on Flex/Bison (tools for building compilers)

## Slide 27: Evaluation
Microbenchmark
  Control loop delay
  Stability and fast convergence of NetVRM
Macrobenchmark
  Generality
  Impact of allocation epochs
  Impact of workload parameters
  NetVRM in datacenter network

## Slide 28: Evaluation
Microbenchmark
  Control loop delay
  Stability and fast convergence of NetVRM
Macrobenchmark
  Generality
  Impact of allocation epochs
  Impact of workload parameters
  NetVRM in datacenter network

## Slide 29: Control loop delay
0
32 64 128 256
Number of concurrent applications
5
10
15
Delay (ms)
Fetch Calc
Reconfig Runtime
One reallocation can be done in ~10 ms
Reconfig dominates the control loop
The time to complete a virtual memory reallocation.
Runtime: the runtime overhead for resetting the state (e.g., counters)

## Slide 30: Macrobenchmark
NetVRM configuration and network topology
  Allocation epoch and measurement epoch are one second
  Each application has traffic from 4 switches independently
NetVRM applications
  Heavy hitter detection (HH)
  Newly opened TCP connection detection (NO)
  Superspreader detection (SS)
    Sources that connect to a large number of distinct destinations
  Sketch-based heavy hitter detection (SHH)
Traces
  2019 passive CAIDA traces
Alternative approaches
  Equal-All: statically assigns an equal amount of register memory to all applications
  Equal-Active: equally assigns register memory to active instances

## Slide 31: Generality
NetVRM outperforms alternatives on both the mean and the tail
NetVRM is general to different network application types
Each application has traffic from four switches independently
Satisfaction ratio as the performance metric
Alternatives: Equal-All, Equal-Active

## Slide 32: Impact of allocation epochs
2
4 8
Allocation epoch (s)
16
1.0
0.8
0.6
0.4
0.2
0
Mean
5% tail
Drop ratio
Reject ratio
A shorter allocation epoch leads to a better performance

## Slide 33: Conclusion
NetVRM supports dynamic register memory sharing between multiple concurrent applications on a programmable network
  Virtual register memory: enable online register memory sharing
  Dynamically allocate memory for better resource efficiency
  P4VRM: easily equip the programs with virtual register memory

## Slide 34
Thank you!