## Slide 1: CSE5095-002: Topics in Software Defined Networking
Lecture 6
Minmei Wang
Computer Science and Engineering

## Slide 2: Forwarding Metamorphosis: Fast Programmable Match-Action Processing in Hardware for SDN Pat Bosshart, Glen Gibb, Hun-Seok Kim, George Varghese, Nick McKeown, Martin Izzard, Fernando Mujica, Mark Horowitz Texas Instruments, Stanford University, Microsoft

## Slide 3: Outline
Conventional switch chips are inflexible
SDN demands flexibility…sounds expensive…
How do we do it: The RMT switch model
Flexibility costs less than 15%

## Slide 4: Fixed function switch

## Slide 5: What if you need flexibility?
Flexibility to:
  Add a new header field
  Specify the number, topology, widths, and depths of match tables
  Add a new table
  Add a different action
  ......
SDN accentuates the need for flexibility
  Gives programmatic control to control plane, expects to be able to use flexibility

## Slide 6: What does SDN want?
Multiple stages of match-action
  Flexible allocation
Flexible actions
Flexible header fields

## Slide 7: What We Set Out To Learn
How do I design a flexible switch chip?
What does the flexibility cost?
  Balance the flexibility and speed

## Slide 8: Outline
Conventional switch chip are inflexible
SDN demands flexibility…sounds expensive…
How do we do it: The RMT switch model
Flexibility costs less than 15%

## Slide 9: RMT model
Very long instruction word (VLIW): instruction set architectures designed to exploit instruction level parallelism (ILP)

## Slide 10: RMT model
Very long instruction word (VLIW): instruction set architectures designed to exploit instruction level parallelism (ILP)

## Slide 11: The RMT Abstract Model
Parse graph
Table graph

## Slide 12: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
IPV6
TCP
UDP
Ethernet IPV4 TCP
Packet:
protocol
EtherType

## Slide 13: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
TCP
UDP
Ethernet IPV4 TCP
Packet:

## Slide 14: Reconfigurable Match Tables: The Table Graph
VLAN
MAC
FORWARD
IPV4-DA
ETHERTYPE
RCP
ACL
IPV6-DA

## Slide 15: Changes to Parse Graph and Table Graph
Ethernet
IPV4
TCP
UDP
Done
ACL
L2S
L2D
IPV4-DA
ETHERTYPE
Table Graph
VLAN
VLAN
IPV6-DA
IPV6
RCP
RCP
Parse Graph
MY-TABLE

## Slide 16: Performance V.S. Flexibility
Change to pipeline
Fixed function chips specialize processors
Flexible switch needs general purpose CPUs

## Slide 17: How We Did It
Memory
C
P
U
CPU
CPU
C
P
U
CPU
CPU
CPU
CPU
CPU
Memory to CPU bottleneck
Replicate CPUs
More stages for finer granularity
Higher CPU cost ok
C
P
U
CPU
CPU

## Slide 18: RMT Logical to Physical Table Mapping
TCAM
640b
640b
Physical
Stage n
Physical
Stage 2
Logical Table 1
Ethertype
Logical Table 6
L2D
8 UDP
2
VLAN
3
IPV4
5
IPV6
4
L2S
7 TCP
SRAM
HASH
Physical
Stage 1
ACL
UDP
TCP
L2S
L2D
IPV4
ETH
VLAN
IPV6
9 ACL
Table Graph
Action
Match Table
Action
Match Table
Action
Match Table
Notes: To make it possible to efficiently use multiple stages of match tables, it is assumed that the RMT Model can be configured to map Logical Tables to the Physical Tables.
To create bigger tables, one table may traverse multiple stages.
To create many smaller tables, several tables can be packed into one stage.
To make the allocation even more flexible, the Action instructions and the Statistic could share the same table space.
This slide gives a crude representation of how the the Logical Tables could be mapped to the Physical Tables.
In practice, the control plane would need to create a Table Flow Graph (to accompany the Parse Graph) to decide how the Logical Tables are mapped.
The control plane is assumed to know the number and size of the physical stages available.
There could be as few as 1 stage. A given switch might only allow Logical Tables to directly correspond to Physical Tables.

## Slide 19: TCAM
Ternary content-addressable memory
  A specialized type of high-speed memory that searches its entire content sin a single clock cycle
  Three states: 0,1, X (don’t care)
  Entry: data & mask
  Support arbitrary lookup key
  E.g., 10XX0

## Slide 20: Action Processing Model
Instruction
ALU
Match result
Header In
Field
Header Out
Field
Data
Notes: Action processing is assumed to be available in each physical stage of the pipeline.
The headers are available along with the match result and metadata. Optional state could be available to the Action Processors.
There are assumed to be some number of processors (could be 1, could be hundreds) to perform Actions on headers.
The Action instruction set is assumed to be protocol independent (e.g. “insert these 8 bits starting at bit 19 of the 3rd header”).

## Slide 21
ALU
VLIW Instructions
Match result
Modeled as Multiple VLIW CPUs per Stage
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU

## Slide 22: Our Switch Design
64 x 10Gb ports
  960M packets/second
  1GHz pipeline
Programmable parser
32 Match/action stages
Huge TCAM: 10x current chips
  64K TCAM words x 640b
SRAM hash tables for exact matches
  128K words x 640b
224 action processors per stage
All OpenFlow statistics counters

## Slide 23: Outline
Conventional switch chip are inflexible
SDN demands flexibility…sounds expensive…
How do I do it: The RMT switch model
Flexibility costs less than 15%

## Slide 24: Cost of Configurability: Comparison with Conventional Switch
Many functions identical: I/O, data buffer, queueing…
Make extra functions optional: statistics
Memory dominates area
  Compare memory area/bit and bit count
RMT must use memory bits efficiently to compete on cost
Techniques for flexibility
  Match stage unit RAM configurability
  Ingress/egress resource sharing
  Table predication allows multiple tables per stage
  Match memory overhead reduction
  Match memory multi-word packing

## Slide 25: Chip Comparison with Fixed Function Switches
Section | Area % of chip | Extra Cost
IO, buffer, queue, CPU, etc | 37% | 0.0%
Match memory & logic | 54.3% | 8.0%
VLIW action engine | 7.4% | 5.5%
Parser + deparser | 1.3% | 0.7%
Total extra area cost |  | 14.2%
Section | Power % of chip | Extra Cost
I/O | 26.0% | 0.0%
Memory leakage | 43.7% | 4.0%
Logic leakage | 7.3% | 2.5%
RAM active | 2.7% | 0.4%
TCAM active | 3.5% | 0.0%
Logic active | 16.8% | 5.5%
Total extra power cost |  | 12.4%
Area
Power

## Slide 26: Conclusion
How do we design a flexible chip?
  The RMT switch model
  Bring processing close to the memories:
    pipeline of many stages
  Bring the processing to the wires:
    224 action CPUs per stage
How much does it cost?
  15%
Lots of the details how we designed this in 28nm CMOS are in the paper