## Slide 1: CSE5095-002: Topics in Software Defined Networking
Lecture 8
Minmei Wang
Computer Science and Engineering
Some slides are borrowed from P4 tutorials.

## Slide 2: Outlines
What is data plane programming
Introduction to P4
P4 runtime
Resources

## Slide 3: What is Data Plane Programming?
2
Copyright © 2018 – P4.org
Why program the Data Plane?

## Slide 4: Software Defined Networking: Logically Centralized Control
Copyright © 2018 – P4.org
3
Main contributions
  OpenFlow = standardized model
    match/action abstraction
  OpenFlow = standardized protocol to interact with switch
    download flow table entries, query statistics, etc.
Concept of logically centralized control via a single entity (“SDN controller”)
  Simplifies control plane – e.g. compute optimal paths at one location (controller), vs. waiting for distributed routing algorithms to converge
Issues
  Data-plane protocol evolution requires changes to standards (12 → 40 OpenFlow match types)
  Limited interoperability between vendors => southbound I/F differences handled at controller (OpenFlow / netconf / JSON / XML variants)
SDN
Controller
Switch
Southbound I/F
x n
Control Function (“App”) x m
Northbound I/F
x 1

## Slide 5: Status Quo: Bottom-up design
Copyright © 2018 – P4.org
Switch OS
Run-time API
Driver
“This is how I know to process packets”
(i.e. the ASIC datasheet makes the rules)
Fixed-function ASIC
4
?
Network Demands

## Slide 6: A Better Approach: Top-down design
Copyright © 2018 – P4.org
Switch OS
5
Network Demands
Feedback
Run-time API
Driver
P4
“This is how I want the network to behave and how to switch packets…”
(the user / controller makes the rules)
P4 Programmable Device

## Slide 7: Benefits of Data Plane Programmability
Copyright © 2018 – P4.org
New Features – Add new protocols
Reduce complexity – Remove unused protocols
Efficient use of resources – flexible use of tables
Greater visibility – New diagnostic techniques, telemetry, etc.
SW style development – rapid design cycle, fast innovation, fix data plane bugs in the field
You keep your own ideas
Think programming rather than protocols…

## Slide 8: Programmable Network Devices
Copyright © 2018 – P4.org
PISA: Flexible Match+Action ASICs
  Intel Flexpipe, Cisco Doppler, Cavium (Xpliant), Barefoot Tofino, …
NPU
  EZchip, Netronome, …
CPU
  Open Vswitch, eBPF, DPDK, VPP (vector packet processor)…
    eBPF: Berkeley Packet Filter: packet analysis
FPGA
  Xilinx, Altera, …
These devices let us tell them how to process packets.

## Slide 9: What can you do with P4?
Copyright © 2018 – P4.org
Layer 4 Load Balancer – SilkRoad[1]
Low Latency Congestion Control – NDP[2]
In-band Network Telemetry – INT[3]
Fast In-Network cache for key-value stores – NetCache[4]
Consensus at network speed – NetPaxos[5]
Aggregation for MapReduce Applications [6]
Network measurement tasks – PINT [7]
Distributed machine learning – SwitchML [8], ATP [9]
… and much more
[1] Miao, Rui, et al. "SilkRoad: Making Stateful Layer-4 Load Balancing Fast and Cheap Using Switching ASICs." SIGCOMM, 2017.
[2] Handley, Mark, et al. "Re-architecting datacenter networks and stacks for low latency and high performance.” SIGCOMM, 2017.
[3] Kim, Changhoon, et al. "In-band network telemetry via programmable dataplanes.” SIGCOMM. 2015.
[4] Xin Jin et al. “NetCache: Balancing Key-Value Stores with Fast In-Network Caching.” To appear at SOSP 2017
[5] Dang, Huynh Tu, et al. "NetPaxos: Consensus at network speed.” SIGCOMM, 2015.
[6] Sapio, Amedeo, et al. "In-Network Computation is a Dumb Idea Whose Time Has Come." Hot Topics in Networks. ACM, 2017.
[7] Ben Basat, Ran, et al. PINT: Probabilistic in-band network telemetry, In Proc. of ACM SIGCOMM, 2020.
[8] Sapio, Amedeo, et al. "Scaling distributed machine learning with in-network aggregation." in Proc. of USENIX NSDI 2021.
[9] Lao, ChonLam, et al. "{ATP}: In-network Aggregation for Multi-tenant Learning.“ in Proc. of USENIX NSDI 2021.

## Slide 10: Brief History and Trivia
Copyright © 2018 – P4.org
May
July
Aug
Sep
Jan
Mar
Nov
May
Apr
Dec
May
2013:
2014:
2014:
2014:
2015:
2015:
2016:
2017:
Initial idea and the name “P4” First paper (SIGCOMM CCR)
First P414 Draft Specification (v0.9.8) P414 Specification released (v1.0.0) P414 v1.0.1
P414 v1.0.2 P414 v1.0.3 P414 v1.0.4
P416 – first commits
First P416 Draft Specification P416 Specification released
2016:
2016:
2017:

## Slide 11: Introduction to P4

## Slide 12: P4
P4 is a higher-level language for Programming Protocol-independent Packet Processors

## Slide 13: PISA: Protocol-Independent Switch Architecture
Programmable Parser
Programmable Deparser
Programmable Match-Action Pipeline
Programmer declares the headers that should be recognized and their order in the packet
Programmer defines the tables and the exact processing algorithm
Programmer declares how the output packet will look on the wire
Copyright © 2018 – P4.org

## Slide 14: PISA in Action
Programmable Parser
Programmable Deparser
Packet is parsed into individual headers (parsed representation)
Headers and intermediate results can be used for matching and actions
Headers can be modified, added or removed
Packet is deparsed (serialized)
Programmable Match-Action Pipeline
Copyright © 2018 – P4.org

## Slide 15: P416 Language Elements
Architecture Description
Extern Libraries
Programmable blocks and their interfaces
Support for specialized components
Data Types
Bistrings, headers, structures, arrays
Controls
Tables, Actions, control flow statements
Parsers
Expressions
Copyright © 2018 – P4.org
Basic operations and operators
State machine, bitfield extraction

## Slide 16: Parsers
Parsers describe the permitted sequences of headers within received packets

## Slide 17: Parsers
Parsers describe the permitted sequences of headers within received packets

## Slide 18
Copyright © 2018 – P4.org
The fundamental unit of a Match-Action Pipeline
  Specifies what data to match on and match kind
  Specifies a list of possible actions
  Optionally specifies a number of table properties
    Size
    Default action
    Static entries
    etc.
Each table contains one or more entries (rules)
An entry contains:
  A specific key to match on
  A single action that is executed when a packet matches the entry
  Action data (possibly empty)
35
Controls - Tables

## Slide 19: Tables: Match-Action Processing
Copyright © 2018 – P4.org
Directional (DataPlane) Parameters
Directionless (Action Data) Parameters
Action Code
Action Execution
Lookup Key
Key | Action ID | Action Data
Default Action ID
Default Action Data
Hit
Data
Headers and Metadata (Input)
Headers and Metadata (Output)
Action ID
Hit/Miss
Selector
Control Plane
Headers and Metadata

## Slide 20: Example: IPv4_LPM Table
Data Plane (P4) Program
  Defines the format of the table
    Key Fields
    Actions
    Action Data
  Performs the lookup
  Executes the chosen action
Control Plane (IP stack,
Routing protocols)
Populates table entries with specific information
  Based on the configuration
  Based on automatic discovery
  Based on protocol calculations
Key | Action | Action Data
10.0.1.1/32 | ipv4_forward | dstAddr=00:00:00:00:01:01 port=1
10.0.1.2/32 | drop | 
*` | NoAction | 
10.0.1.1
Copyright © 2018 – P4.org
10.0.1.2

## Slide 21: IPv4_LPM Table
table ipv4_lpm { key = {
hdr.ipv4.dstAddr: lpm;
}
actions = { ipv4_forward; drop; NoAction;
}
size = 1024;
default_action = NoAction();
}
Copyright © 2018 – P4.org

## Slide 22: Match Kinds
/* core.p4 */ match_kind {
exact, ternary, lpm
}
/* v1model.p4 */ match_kind {
range,
selector
}
/* Some other architecture */ match_kind {
regexp, fuzzy
}
Copyright © 2018 – P4.org
The type match_kind is special in P4
The standard library (core.p4) defines three standard match kinds
  Exact match
  Ternary match
  LPM match
The architecture (v1model.p4) defines two additional match kinds:
  range
  selector
Other architectures may define (and provide implementation for) additional match kinds
Selector: dynamic action selection

## Slide 23: Defining Actions for L3 forwarding
/* core.p4 */ action NoAction() {
}
/* basic.p4 */ action drop() {
mark_to_drop();
}
/* basic.p4 */
action ipv4_forward(macAddr_t dstAddr,
bit<9> port) {
...
}
Copyright © 2018 – P4.org

## Slide 24: Controls
Control flow
  Describes packet-processing
  steps on a target

## Slide 25: Applying Tables in Controls
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
table ipv4_lpm {
...
}
apply {
...
ipv4_lpm.apply();
...
}
}
Copyright © 2018 – P4.org

## Slide 26: Extern objects and functions
P4 programs can also interact with objects and functions provided by the architecture
  extern construct describes the interfaces exposed to the data plane
Checksum operations offered by an incremental checksum unit

## Slide 27: P416 Deparsing
/* From core.p4 */ extern packet_out {
void emit<T>(in T hdr);
}
/* User Program */
control DeparserImpl(packet_out packet,
in headers hdr) {
apply {
...
packet.emit(hdr.ethernet);
...
}
}
Copyright © 2018 – P4.org
Assembles the headers back into a well-formed packet
Expressed as a control function
  No need for another construct!
packet_out extern is defined in core.p4: emit(hdr): serializes header if it is valid
Advantages:
Makes deparsing explicit...
...but decouples from parsing

## Slide 28: P4_16 Approach
Community-Developed
Term | Explanation
P4 Target | An embodiment of a specific hardware implementation
P4 Architecture | Provides an interface to program a target via some set of P4-programmable components, externs, fixed components
P416
Language
P416 Core
Library
Vendor-supplied
Extern Libraries
Architecture Definition
Copyright © 2018 – P4.org

## Slide 29: Example Architectures and Targets
Copyright © 2018 – P4.org
15
TM
TM
TM
V1Model (BMv2 Simple Switch)
Anything
SimpleSumeSwitch
Portable Switch Architecture (PSA)
The SimpleSumeSwitch is the P4 architecture that is currently defined for the NetFPGA SUME.
As an analogy, the PSA is to the P416 language as the C standard library is to the C programming language.

## Slide 30: V1 model
Load balance based on ECMP
  https://github.com/p4lang/tutorials/blob/master/exercises/load_balance/solution/load_balance.p4

## Slide 31: Tips for writing P4 code
V1 model
  https://github.com/p4lang/p4c/blob/main/p4include/v1model.p4

## Slide 32: P4 compiler

## Slide 33: P4 compiler
https://github.com/p4lang/p4c/tree/main/backends

## Slide 34: P4Runtime
8

## Slide 35: Runtime control of P4 data planes
P4 Program
P4 Architecture Model
P4 Compiler
Target-specific configuration binary
Control Plane
Data Plane
Tables
Extern objects
Load
Vendor supplied
User supplied
Add/remove table entries
CPU port
Packet-in/out
Extern control
Focus of this session
9
Copyright © 2018 – P4.org, ONF

## Slide 36: What is P4Runtime?
Framework for runtime control of P4 targets
  Open-source API + server implementation
https://github.com/p4lang/PI
  Initial contribution by Google and Barefoot
Work-in-progress by the p4.org API WG
Protobuf-based API definition
  p4runtime.proto
  gRPC transport
P4 program-independent
  API doesn’t change with the P4 program
13

## Slide 37: Protocol Buffers (protobuf) Basics
14
Copyright © 2018 – P4.org, ONF
Language for describing data for serialization in a structured way
Common binary wire-format
Language-neutral
  Code generators for: Action Script, C, C++, C#, Clojure, Lisp, D, Dart, Erlang, Go, Haskell, Java, Javascript, Lua, Objective C, OCaml, Perl, PHP, Python, Ruby, Rust, Scala, Swift, Visual Basic, ...
Platform-neutral
Extensible and backwards compatible
Strongly typed

## Slide 38: Protocol Buffers (protobuf) Basics
14

## Slide 39: gRPC Basics
Use Protocol Buffers to define service API and messages
Automatically generate native stubs in:
  C / C++
  C#
  Dart
  Go
  Java
  Node.js
  PHP
  Python
  Ruby
Transport over HTTP/2.0 and TLS
  Efficient single TCP connection implementation that supports bidirectional streaming
15
Copyright © 2018 – P4.org, ONF
More details here: https://grpc.io/docs/guides/

## Slide 40: What is P4Runtime?
13

## Slide 41: P4Runtime Service
17
Copyright © 2018 – P4.org, ONF
Enables a local or remote entity to arbitrate mastership, load the pipeline/program, send/receive packets, and read and write forwarding table entries, counters, and other P4 entities.
service P4Runtime {
rpc Write(WriteRequest) returns (WriteResponse) {}
rpc Read(ReadRequest) returns (stream ReadResponse) {}
rpc SetForwardingPipelineConfig(SetForwardingPipelineConfigRequest) returns (SetForwardingPipelineConfigResponse) {}
rpc GetForwardingPipelineConfig(GetForwardingPipelineConfigRequest) returns (GetForwardingPipelineConfigResponse) {}
rpc StreamChannel(stream StreamMessageRequest) returns (stream StreamMessageResponse) {}
}

## Slide 42: P4Runtime Service
18
Copyright © 2018 – P4.org, ONF
P4Runtime Protobuf Definition:
https://github.com/p4lang/p4runtime/blob/master/proto/p4/v1/p4runtime.proto
Service Specification:
https://p4.org/p4-spec/p4runtime/main/P4Runtime-Spec.html

## Slide 43: P4Info example
...
action ipv4_forward(bit<48> dstAddr,
bit<9> port) {
/* Action implementation */
}
...
table ipv4_lpm { key = {
hdr.ipv4.dstAddr: lpm;
}
actions = {
ipv4_forward;
...
}
...
}
basic_router.p4
actions {
id: 16786453
name: "ipv4_forward" params {
id: 1
name: "dstAddr" bitwidth: 48
...
id: 2
name: "port" bitwidth: 9
}
}
...
tables {
id: 33581985
name: "ipv4_lpm" match_fields {
id: 1
name: "hdr.ipv4.dstAddr" bitwidth: 32
match_type: LPM
}
action_ref_id: 16786453
}
basic_router.p4info
P4 compiler
22

## Slide 44: Local control
Local control plane
OSPF
BGP
P4-defined protocol
etc.
table_entry { table_id: 33581985 match {
field_id: 1 lpm {
value: "\f\000\... prefix_len: 8
}
}
action {
action_id: 16786453 params {
param_id: 1 value: "\000\0...
}
params { param_id: 2
value: 7
}
}
}
Same target-independent protobuf format
p4info
p4info
P4 target
The P4Runtime API can be used equally well by a remote or local control plane
29
Copyright © 2018 – P4.org, ONF

## Slide 45: Remote control
Vendor A
Vendor B
Vendor C
Remote control plane
OSPF
BGP
P4-defined custom protocol
etc.
table_entry { table_id: 33581985 match {
field_id: 1 lpm {
value: "\f\000\... prefix_len: 8
}
}
action {
action_id: 16786453 params {
param_id: 1 value: "\000\0...
}
params { param_id: 2
value: 7
}
}
}
Target-independent protobuf format
p4info
p4info
p4info
p4info
28
Copyright © 2018 – P4.org, ONF

## Slide 46: Behavior model
BM runtime API
  Command line interface (CLI) program to manipulate MATs
  https://github.com/p4lang/behavioral-model
  List of supported commands
    table_set_default <table name> <action name> <action parameters>
    table_add <table name> <action name> <match fields> => <action parameters> [priority]
    table_delete <table name> <entry handle>

## Slide 47: Behavior model
BM runtime API
  Command line interface (CLI) program to manipulate MATs
  https://github.com/p4lang/behavioral-model
Simple router

## Slide 48: Barefoot runtime interface
BfRt API
  C, C++, Python

## Slide 49: Resources and platform
Behavioral model (BMv2 simple switch)
  A tool for developing, testing, and debugging P4 data planes and control plane software
  https://github.com/p4lang/behavioral-model
  https://github.com/p4lang/tutorials
  Run using VirtualBox
Hardware switch
  E.g., Tofino Switch
  Intel ICRP

## Slide 50: Resources and platform
ICRP
https://github.com/barefootnetworks/Open-Tofino

## Slide 51: Resources and platform
https://github.com/barefootnetworks/Open-Tofino