## Slide 1: CSE5095-002: Topics in Software Defined Networking
Lecture 9
Minmei Wang
Computer Science and Engineering
Some slides are borrowed from the presentations of the original two papers listed in the next slide.

## Slide 2: SDN and Virtualization
“Can the Production Network Be the Testbed?” (FlowVisor), OSDI, 2010
“Network Virtualization in Multi-tenant Datacenters,” NSDI 2014

## Slide 3: Motivation – efficient way to evaluate new research ideas
Can we build a testbed that is embedded into every switch and router of the production network?

## Slide 4: FlowVisor
A way to build a testbed that is embedded in and grows with the network
  Run on deployed hardware and at real line-rates
    Software slicing layer
  Allow real users to opt-in on a per-flow basis
    Use a policy language to map flows to slices
  Port easily to non-sliced networks
    FlowVisor is transparent to both data and control planes
  Enforce strong isolation between slices
  Operate on deployed networks

## Slide 5: FlowVisor Overview
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
Controller 1
App
App
Controller
2
Virtualization (FlowVisor)
App
OpenFlow
Controller 1
Controller 1
Controller
2
Controller
2

## Slide 6: FlowVisor overview

## Slide 7: FlowVisor overview
Divide the production network into logical slices
Example of network slices

## Slide 8: FlowVisor overview
Divide the production network into logical slices
  Network resources are sliced
    Topology, bandwidth, forwarding table entries, device CPU
  Each slice has own distinct control logic
    Each slice owner implements its control logic as an OpenFlow controller
  Slices are defined using a slice definition policy language
Enforce strong isolation between slices
    Actions in one slice do not affect another slice

## Slide 9: Network slice and flowspace
A network slice controls a subset of traffic
The subset is defined by a collection of packet headers.
  n-bit headers has n-dimension space – flowspace
Example:
  HTTP traffic – TCP port = 80
  All traffic from node 127.2.1.12 – IP_SRC=127.2.1.12
A subset of flowspace + a subset of topology + control logic = network slice

## Slide 10: Properties of Flowspace
Backwards compatible
  No end points need to change
Easily implemented in hardware
  e.g., TCAM flow-table in each switch
Strong isolation of flows
  Simple geometric construction
  Can prove which flows can/cannot communicate

## Slide 11: Slicing Example

## Slide 12: Slicing Network Resources
Topology
Forwarding tables
Bandwidth
Device CPU

## Slide 13: Slicing Network Resources
Topology
  Each slice has its own view of network nodes and the connectivity between them
Forwarding tables
  Each slice has a finite quota of forwarding rules
    E.g., TCAM entries

## Slide 14: Slicing Network Resources – Device CPU isolation
OF abstraction: process scheduling and rate-limiting
  New flow messages sent to the controller
    Use rate limit to control the new flow message arrival rate
      Track, drop the packets if it exceeds some threshold
  Controller requests
    Throttle the OpenFlow message rate to a maximum rate per second for each slice
  Slow-path forwarding
    Rewrite to one-time packet forwarding events (then rate limit)
  Internal bookkeeping (e.g., update internal counters)
    Reserve sufficient CPU

## Slide 15: Slicing Network Resources – bandwidth isolation
Create a per-slice queue on each port on the switch
  Queue is configured for a fraction of link bandwidth
Sent out port X
Sent out queue Y on port X

## Slide 16
OpenFlow
Protocol
FlowVisor
Broadcast
Multicast
OpenFlow
Protocol
http
Load-balancer
FlowVisor Slicing Example
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch

## Slide 17
OpenFlow Protocol
FlowVisor Slicing Example (Cont’d)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Network Administrator’s
FlowVisor
OpenFlow Protocol
Production
Network
Controller
Alices’s
FlowVisor
GENI’s
FlowVisor
Bob’s
FlowVisor
Learning
switch
Mobile VMs
New BGP
LTE-WiFi
Handover
Tricast Lossless
Handover
Hierarchical slicing

## Slide 18
FlowVisor Implemented on OpenFlow
Custom
Control
Plane
Network
Stub
Control
Plane
Data
Plane
Server
OpenFlow Controller
OpenFlow
Protocol
OpenFlow
Firmware
Data Path
Switch/
Router
Servers
OpenFlow OpenFlow OpenFlow
Controller Controller Controller
OpenFlow
FlowVisor
OpenFlow
OpenFlow
Firmware
Data Path
Switch/
Router

## Slide 19
FlowVisor Message Handling
Alice Bob
Controller Controller
OpenFlow
Rule
Cathy
Controller
Policy Check:
Is this rule allowed?
Full Line Rate Forwarding
Packet
FlowVisor
OpenFlow
Exception
OpenFlow
Firmware
Data Path
Policy Check:
Who controls this packet?
Source: R. Sherwood

## Slide 20: Evaluation
Scalability
Linear growth with new flow rate

## Slide 21: Evaluation
Scalability
Linear growth with number of rule per-slide
Fluctuation with observed workload

## Slide 22: Evaluation
Scalability
Linear growth with number of slices
Fluctuation with observed workload

## Slide 23
Conclusion
• Network slicing can help perform more realistic evaluations and support multiple tenants
• FlowVisor allows experiments to run concurrently but safely on the production network
• Currently limited to subsets of actual topology
  - Add virtual links, nodes support

## Slide 24: SDN and Virtualization
“Can the Production Network Be the Testbed?” (FlowVisor), OSDI, 2010
“Network Virtualization in Multi-tenant Datacenters,” NSDI 2014

## Slide 25: NETWORK VIRTUALIZATION?
~1985
Late 1990s
1993 1995+
2010
Network Elements
VLAN NAT MPLS VRF as VMs FlowVisor
~2005
VLAN | NAT | MPLS | VRF | Elements as VMs | FlowVisor
Subnet | IP address space | Path | L3 FIB | Elements | ASIC
Plenty of primitives but no network virtualization per se.

## Slide 26: MULTI-TENANT DATACENTERS
Compute Virtualization Layer
Operationally intensive
…
Result with the aforementioned primitives:
Slow provisioning • Mobility is limited
Limited VM placement • Hardware dependent

## Slide 27: NETWORK HYPERVISOR
Standard x86
Standard IP connectivity
VMs
Server Hypervisor
Logical Networks
Network Hypervisor
Decoupled
App
App
App
App
App
App
App
x86
Workload
Workload
Workload
Workload
Workload
Workload
Workload
L2, L3, L4-L7 Services

## Slide 28: AGENDA
Overall design of NVP network hypervisor.
Design challenges.
Hard lessons learnt.

## Slide 29: WHAT IS A NETWORK HYPERVISOR?
Packet Abstraction
Mgmt Mgmt Mgmt
Control Abstraction
Packet Abstraction + Control Abstraction = Network Hypervisor
Logical Network
Network Hypervisor
Logical Network
Logical Network

## Slide 30: WHAT ARE THE ABSTRACTIONS?
Packet abstraction
Compliance with standard TCP/IP stack is a necessity:
Control abstraction
Allow tenants to define a set of logical network elements that they can configure
Networking has no single high level control interface
There is a low-level one
Packet In
Packet Out
ACL
L2
L3
ACL
L2, L3 semantics (unicast, ARP, …)
Tenant’s Control Plane
Logical Datapath

## Slide 31: GENERALITY OF DATAPATH
ACL
L2
L3
ACL
ACL
L2
ACL
ACL
L2
ACL
Switch CP Router CP Switch CP
Datapath Datapath Datapath
One logical switch
2-tier logical topology
Arbitrary logical topology
Faithful reproduction of physical network service model.

## Slide 32: WHERE TO IMPLEMENT?
Network Core
•
•
•
Independence from physical hardware.
Programmatic control. Operational model of compute virtualization.
No extra x86 hops: just the source and destination hypervisor!
Tenant CP
Network Hypervisor

## Slide 33: WHAT IS A NETWORK HYPERVISOR?
Packet Abstraction
Mgmt Mgmt Mgmt
Control Abstraction
Packet Abstraction + Control Abstraction = Network Hypervisor
Logical Network
Network Hypervisor
Logical Network
Logical Network

## Slide 34: INSIDE THE VIRTUAL SWITCH
ACL
L2
L3
ACL
Datapath
ACL
L2
ACL
Datapath
ACL
L2
ACL
Datapath
OF
OF
OF
OF
OF
OF
OF
OF
OF
OF
OF
OF
OF
Logical Topology First-hop vSwitch
OF
Identify logical ingress port
Execute 1st logical datapath
Determine the next logical datapath
2nd logical datapath
Determine the next…
3rd logical datapath
Send to tunnel

## Slide 35: COMPUTATIONAL CHALLENGE
Controllers learn the location of VMs.
Controllers proactively compute & push all forwarding state required to connect each VM.
Forwarding State = F(configuration,VM locations)
Repeat above as logical configuration or physical configuration (VM placement) changes.
Challenge: How to compute O(N2) volume of low-level OpenFlow and OVSDB state, when inputs change all the time.

## Slide 36: STATE COMPUTATION Forwarding State = F(configuration, VM locations)
1. How to Scale Computation
Incremental computation and pushing for quick updates.
2. How to Guarantee Correctness
Avoid all handwritten finite state machines, machine generated instead.
Datalog based declarative language to program F.
Shard the computation across controller cluster.

## Slide 37: LESSONS LEARNT: ABSTRACTIONS
Assumptions about logical network structure often embedded into the workload.
A single L2 domain sufficient for initial, simple workloads.
To support more complex workloads without changing them, more complex logical topologies become a necessity.
A logical switch
“Basic Enterprise App”
Two tier logical network
“Modern App”
Arbitrary logical network
“Bank”

## Slide 38: LESSONS: FAILURE ISOLATION
Two Channels, No Atomic Updates
Proactive pushing of all state not enough to decouple controllers from data plane.
Connection may die while pushing updates.
One Channel, Atomic Updates
Atomically applied, batched updates.
Connection failure does not result in incomplete state.
Batch 2
Batch 1
Batch N
OpenFlow
OVSDB
Data plane may operate over incomplete state!
At most old state.
Custom Protocol

## Slide 39: LESSONS: SCALING
OPENFLOW IS EXPENSIVE
Too primitive
Simple operations take several flow entries.
For example, tunnel failover, encapsulation header ops.
Lots of redundancy.
Too tightly coupled
Each switch requires some flow customization; can’t just blindly replicate flows.
To compute flow entries, may have to wait for responses from the OVS configuration database.
Replace a OF & OVSDB with a network virtualization specific protocol.
OpenFlow becomes a protocol internal to the hypervisor.

## Slide 40: Conclusion
Openflow can facilitate network virtualization
The current practice of network virtualization is not ideal. This paper presents a limited form of network virtualization for special cases.